## Slide 1: BT-15

## Slide 4: Vultee BT-15
General Characteristics
Crew: 2
Length: 29 ft 1 in
Wingspan: 42 ft 0 in
Height: 12 ft 4 3/8 in
Wing area: 239 sq ft
Empty weight: 3,305 lb
Max Gross weight: 4,350 lb
Powerplant: 1 × Wright R-975-11
nine-cylinder air-cooled radial engine, 440 hp
Performance
Range: 525 mi (1950 rpm, 27 gph, 10 gal TO, no reserve)
Service ceiling: 21,650 ft
4

## Slide 6: BT-15
6
General
Fuel: 60 gallons per side, 17 gallons of 60 is reserve on right side
Oil: 8.5 gallons (normal), 10.9 (overflow).
Normal Takeoff use 20º flaps
Climb at 90mph until flaps are retracted, then 100mph
Mag check 1700 rpm, max 100 drop
Field Baro Check at 2150 RPM
Maximum Baggage Capacity 175 pounds

## Slide 7: BT-15
All in MPH
90 works for everything
  Vy 90 with 20 flaps
  Vy 100 with flaps up
  Vne 207
  Vno 177
  Vfe 111
  Vs 72
  Vso 30 flap 65
  Vso 60 flap 62
7
Speeds

## Slide 8: BT-15
8
Power Settings
Takeoff Full/2250 1minute
METO Full/2200 cont.
Climb 31/2100
Cruise 26/1900

## Slide 9: BT-15
9
Preflight
4 sumps, one under door.
Bottom intake is oil cooler.
Side intake is carb air inlet.
Make sure that all 3 wires are
secure in bottom of cowl.

## Slide 10: BT-15
As with any radial engine the R-975 can retain oil in the cylinders if not flown for a period of time. Prop should be pulled through 7 blades to ensure all cylinders are cleared.
10
Preflight
Cowling locking bolts and safety wire must be checked prior to flight.

## Slide 11: BT-15
Both front and rear cockpits are equipped with the same instruments.
You cannot start the engine from the rear cockpit.
11
Instruments

## Slide 12: BT-15
The oil tank, located on the firewall, holds 10.9 gallons of oil. Normal operation is 8.5 gallons.
12
Oil
Aeroshell W120

## Slide 14
Select LEFT or RESERVE only!!

## Slide 17: BT-13
Priming is accomplished by pumping the wobble (red handle) until the low fuel pressure light goes out. Then adding prime via the primer located in the upper right of the panel.
17
Priming

## Slide 18: BT-15
The inertia starter is spooled up by holding the starter switch down to the Energize position.
* There is not a need to hold it for an extended period of time.
Start is accomplished by then moving the switch to the up position.
18
Inertia Starter

## Slide 19: BT-15
The inertia starter can be turned by hand in the event battery power is not available. The crank, located in the baggage compartment, is inserted into the inlet.
19
Hand Start
Pilot MUST NOT engage starter until person cranking calls start.

## Slide 20: BT-15
Flap extension speed: 111 MPH
Extension at higher air speeds causes stress on the flap attach points. This can result leaking from the fuel tanks... Or worse.
20
Flaps

## Slide 21: BT-15
Flaps are extended or retracted by turning the yellow crank. Each turn equals 2º of flap movement. May be operated from front or rear cockpit.
21
Flap Extension
Make sure passengers are briefed that the spinning flap handle could hit their ankle if it is placed in the arc of the handle.

## Slide 22: BT-15
22
Unlocking The Tail Wheel

## Slide 23: BT-15
23
Canopy
Passengers should be briefed on the operation of the canopy. To open grasp the yellow handle and twist in either direction. Release to set lock pins.
Canopy can be in any position for any phase of flight.

## Slide 24: BT-15
24
Emergency Exit
Emergency panels are located in both front and rear canopies. Passengers should be briefed on the operation prior to flight.

## Slide 28
Engine fire during start
Keep cranking
Throttle open
Mixture/fuel off
Electrical fire
Avionics off
Alternator off
Master off
Electrical power failure
Conserve battery
Land
Go around
Mixture rich
Take off power
Trim
90 mph
Retract flaps >100’ AGL
100 mph

## Slide 29: BT-15
29
System Questions
What is the fuel capacity?
What is the reserve fuel? Which tank?
What is the maximum flap extension speed?
How many degrees per turn does the flap handle move the flaps?
How is the tail wheel unlocked?
120 gallons
~17 gallons, Right
111 MPH
2º per turn
By turning the aircraft beyond the normal turning arc.

## Slide 30
-----------------------------
{ }

## Slide 31
{ }
{ }

## Slide 33: BT-15
33
System Questions
What is the normal ground run TO distance, 100F, at 500 MSL, with a 10 mph headwind?
What is the normal power setting for TO?
What is the minimum amount of oil?
What is the best glide speed?
What are the stall speeds?
720 feet
Full / 2250 rpm
~7 gallons (not listed)
90MPH
Vs0 72MPH, 30º flaps 65MPH, 60º flaps 62MPH

## Slide 35: BT-13
35
System Questions
What is desired engine oil pressure in flight?
What is the desired engine oil temperature in flight?
What speed is Vne?
What is the maximum gross weight?
What is the maximum baggage weight?
70 to 75 PSI
50 to 70 Degrees C
207 MPH
4350 pounds
175 pounds